## Slide 1: Lab3: Timer
2023.11.16

## Slide 2
Timer:
  TimerHandle_t xTimerCreate
( const char * const pcTimerName, const TickType_t xTimerPeriod,
const UBaseType_t uxAutoReload, void * const pvTimerID,
TimerCallbackFunction_t pxCallbackFunction );
  BaseType_t xTimerStart
( TimerHandle_t xTimer, TickType_t xBlockTime );
  vTaskStartScheduler();

## Slide 3
Timer:
  xTimerStop
( TimerHandle_t xTimer, TickType_t xBlockTime );
  xTimerChangePeriod
( TimerHandle_t xTimer, TickType_t xNewPeriod, TickType_t xBlockTime );
  xTimerDelete
( TimerHandle_t xTimer, TickType_t xBlockTime );
  xTimerReset
( TimerHandle_t xTimer, TickType_t xBlockTime );

## Slide 4: Homework
Basic
  Task 1: count per second (use vTaskDelay)
  Task 2: Create a periodic timer
    per 3 second return

## Slide 5
Bonus
  Create periodic timers which can be started by button (When you press the keypad, timer starts. Otherwise, timer stops.)
    Keypad 1: press and stop after 5 seconds
    Keypad 2: press and stop after 10
seconds

## Slide 6
Scankey:
  #include “Scankey.h”
  OpenKeyPad()
  ScanKey()
詳情請參考 Scankey.zip
1
2

## Slide 7
Use K1 to be input:
  For example: pull low
    Set GPA3 as OUTPUT and set its value as 1
    Set GPA2 as INPUT. Set up
a resistor on the GPA2 and pulling it to ground (or its value will be unstable)

## Slide 8: Demo Time
Place : 創新大樓515 助教 林聖培 (門口有貼座位)
Time :
Tuesday 16:00~ 17:30
Thursday 14:30~ 15:30
Report deadline : 12/1(五) PM 11:59
Demo 必須在 Report deadline 前完成
Demo 前需先上傳程式碼
程式碼上傳格式: LABX_ID_NAME.zip
 main.c + LABX_ID_NAME.docx

## Slide 9: Graded
Basic functions 70%
Bonus 15%
Report & Code 15%